## Slide 1
SMART INDIA HACKATHON 2026 | PROBLEM STATEMENT: SIH26025
MineGuard AI
AI-Enabled Low-Cost Real-Time Mine Subsidence Monitoring, Prediction & Early Warning System
Team MineNova6: Shareque (Lead) | Monika | Aditya | Farhan | Atharva | Affan

## Slide 2
SIH 2026 | PS ID: SIH26025
1. The Underground Coal Mining Subsidence Challenge
40%+ Mining Fatalities
Roof falls & rock caving account for over 40% of fatalities in Indian bord-and-pillar coal mines (Jharia & Raniganj coalfields).
High Cost & Cabling Failure
Existing cabled monitoring costs >₹5 Lakhs/panel. Cables snap during rock movements, disabling safety systems when needed most.
Zero Pre-Collapse Warning
Traditional systems rely on static thresholds that trigger too late, leaving miners zero evacuation time prior to structural roof collapse.

## Slide 3
SIH 2026 | PS ID: SIH26025
2. Proposed Solution — MineGuard AI Ecosystem
Wireless ESP32 LoRa Mesh
₹1,590 low-cost wireless nodes operating on 868MHz frequency band, penetrating rock strata without cables.
AI Subsidence Predictor
Random Forest ML engine correlating 10 parameters (42% weight on 5-min displacement velocity Δdisp/Δt) to detect pre-collapse deformation.
Command Center Dashboard
React + Vite light-theme web application with real-time Leaflet mine map, risk gauges, and dynamic trend curves.
Dual Fail-Safe Alarm Sirens
1kHz local ESP32 buzzer sirens + real-time dashboard notifications + automated alert logging.

## Slide 4
SIH 2026 | PS ID: SIH26025
3. System Architecture & Data Flow
1. Sensors
MPU6050 Tilt/Vib String Pot Load Cell
2. ESP32 Node
ADC Sampling LoRa Packet Payload
3. LoRa Link
868 MHz ISM Long Range Wireless
4. Gateway
SX1276 Receiver HTTP Forwarder
5. FastAPI Backend
REST API SQLite/PostgreSQL
6. AI Risk Engine
Random Forest Risk Score 0-100
7. Command Center
React Dashboard Early Warning Sirens
TECH STACK: React + Vite | Tailwind CSS v4 | Python FastAPI | scikit-learn | Leaflet Maps | ESP32 C++ Arduino

## Slide 5
SIH 2026 | PS ID: SIH26025
4. Technical Innovation & Demonstration Features
Geotechnical Velocity Weighting
Instead of static limits, model evaluates 5-min displacement velocity (Δdisp/Δt) and tilt rate, detecting pre-failure roof sagging in Stage 1.
SIH Emergency Simulator
Includes an interactive SIH Demo controller (Normal State, Warning Drift, Subsidence Event) allowing judges to trigger live emergency escalation on stage.
Multi-Device Synchronized Telemetry
Uses Global Epoch Time seeding and BroadcastChannel API so all judges' phones, laptops, and tablets display identical live numbers.
DGMS Compliance Ready
Designed around Directorate General of Mines Safety guidelines with 3.3V intrinsically safe circuit principles and dual-channel warning alarms.

## Slide 6
SIH 2026 | PS ID: SIH26025
5. Feasibility, Low-Cost Analysis & Scalability
Ultra Low-Cost Hardware BOM (Per Node):
• ESP32 Microcontroller: ₹450
• SX1276 LoRa Radio (868MHz): ₹350
• MPU6050 6-Axis Tilt/Vib Sensor: ₹180
• Linear Displacement String Pot: ₹80
• HX711 + Load Cell: ₹180
• DHT22 Temp/Humidity Sensor: ₹160
• LiFePO4 Battery + TP4056 Charger: ₹150
• TOTAL COST PER NODE: ~ ₹1,590 ($19 USD)
Commercial Advantage & Scalability:
96% Cost Reduction
Commercial cabled sensors cost ₹50,000+ per unit. MineGuard AI delivers a full node array at ₹1,590/node.
Seamless PostgreSQL Scaling
SQLAlchemy ORM allows instant migration from SQLite to PostgreSQL with TimescaleDB time-series indexing for 100+ mine nodes.
Vercel & Cloud Hosted
Web Command Center hosted on Vercel with instant mobile and laptop access for control room engineers.

## Slide 7
Team MineNova6 — Ready for Deployment
Shareque
Team Leader & Tech Lead System Integration & Architecture
Monika
Research & Documentation Lead Geotechnical Domain Analysis
Aditya
UI/UX Design Lead Design System & Glassmorphism
Farhan
Frontend React Engineer Recharts & Leaflet Map Integration
Atharva
Backend FastAPI Lead REST APIs & Database ORM
Affan
AI/ML & Data Lead Random Forest ML Pipeline
MineGuard AI — Protecting Underground Miners in India with AI & Low-Cost Hardware